SECTION 08 4329

ELEPHANT SLIDING DOORS STOREFRONT SYSTEMS

USE THIS SECTION WHEN SPECIFYING BOTTOM ROLLING GLASS SLIDING STOREFRONT SYSTEMS. GLASS IS FURNISHED BY GLAZING SUB-CONTRACTOR AND SPECIFIED IN SECTION 08 80 00.

THIS SPECIFICATION SECTION IS A MANUFACTURER SPECIFIC PRODUCT SPECIFICATION USING THE PROPRIETARY METHOD OF SPECIFYING APPLICABLE TO PROJECT SPECIFICATIONS AND MASTER GUIDE SPECIFICATIONS. THIS SPECIFICATION SECTION SHOULD BE EDITED TO MEET SPECIFIC PROJECT DESIGN CRITERIA BY A KNOWLEDGEABLE CONSTRUCTION SPECIFIER. OPTIONS ARE SHOWN IN BRACKETS [ ]. CHOOSE OPTIONS THAT MEET DESIGN CRITERIA, AND REMOVE BRACKETS AND UNUSED OPTIONS BEFORE PRINTING.

PART 1 – GENERAL

1.01 Section Includes

A. Elephant Door Bottom Rolling Sliding Storefront System.

1.02 Related Requirements

A. Section 05 50 00 - Metal Fabrications

B. Section 08 41 13 - Aluminum Framed Entrances and Storefronts

C. Section 08 42 13 - Aluminum Framed Entrances

D. Section 08 71 00 - Door Hardware

E. Section 08 80 00 - Glazing

1.03 Reference Standards

A. AAMA 2605 - Voluntary Specification, Performance Requirements and Test 	Procedures for Superior Performing Organic Coatings on Aluminum Extrusions and 	Panels; 2005.

B. ASTM A 276 - Standard Specification for Stainless Steel Bars and Shapes; 2008a.

C. ASTM A 314 - Standard Specification for Stainless Steel Billets and Bars for Forging.

D. ASTM A 480 - General Requirements for Flat-Rolled Stainless and Heat-Resisting 	Steel Plate, Sheet, and Strip.

E. ASTM A 563 - Standard Specification for Carbons and Alloy Steel Nuts.

F. ASTM A 666 - Standard Specification for Annealed or Cold-Worked Austenitic 	Stainless Steel 	Sheet, Strip, Plate, and Flat Bar; 2003.

G. ASTM B 221 - Standard Specification for Aluminum and Aluminum-Alloy Extruded 	Bars, Rods, Wire, Profiles, and Tubes; 2006.

H. ASTM B247 - Standard Specification for Aluminum and Aluminum-Alloy Die 		Forgings, Hand Forgings, and Rolled Ring Forgings; 2009.

I. ASTM C 920 - Standard Specification for Elastomeric Joint Sealants; 2005.

J. ASTM C 1036 - Standard Specification for Flat Glass; 2006.

K. ASTM C 1048 - Standard Specification for Heat-Treated Flat Glass--Kind HS, Kind 	FT Coated and Uncoated Glass; 2004.

L. ASTM F 593- Standard Specification for Stainless Steel Bolts, Hex Cap Screws, and 	Studs.

M. ASTM F 594 - Standard Specification for Stainless Steel Nuts.

N. ASTM F1554 - Standard Specification for Anchor Bolts, Steel, 36, 55, and 105-ksi 	Yield Strength.

O. GANA (GM) - GANA Glazing Manual; 2004.

Specifier's Note: Article below includes submittal of relevant data to be furnished by Contractor before, during, and after construction. Coordinate this Article with Architect's and Contractor's duties and responsibilities in Conditions of the Contract and Division 1 Submittal Procedures Section.

1.04 Submittals

A. See Section 01 30 00 - Administrative Requirements, for submittal procedures.

B. Product Data: Manufacturer's descriptive literature for each component in storefront 	entrance assembly.

C. Shop Drawings: Drawings showing layout, dimensions, identification of components, 		and interface with adjacent construction. Coordinate shop drawings with shop drawings 	for glazing specified in Section 08 80 00.

1. Include field measurements of openings.

2. Include scaled (ie., 1 inch = 1 foot) floor plan and reflected ceiling plan of 			sliding 	panel partition layout. Provide dimensions, clearances, material call-outs, 			detail references, and schedule of part numbers, and quantities.

3. Include elevations showing:

a. Appearance of storefront entrance layouts.

b. Locations and identification of manufacturer-supplied door hardware 				and fittings.

c. Locations and sizes of cut-outs and drilled holes for other door 					hardware.

4. Include details of:

a. Rollers.

b. Track assembly.

c. Hardware.

5. Schedule: Listing of each type component in glass panel partition assemblies, 			    including type, size, and thickness of glass used, and, cross-referenced to shop 			    drawing plans, elevations, and details.

D. Selection Samples: Two sets, representing manufacturer's full range of available metal 		     materials and finishes.

E. Certificates: Contractor's certification that installer of sliding glass panel assemblies 	                 meets specified qualifications.

F. Calculations: Design calculations for anchorage. Calculations shall include Engineer's 	                 seal, and signature. Engineer shall be licensed to practice in [California] [State in which 	     the Project is located] [_____________].

G. Operation and Maintenance Data: For manufacturer-supplied operating hardware.

Specifier's Note: Article below to include qualifications, prerequisites, standards, limitations, and criteria to establish the requirements for the level of quality for products and workmanship for the work of this section. Coordinate Article with Division 1 Quality Assurance Section.

1.05 Quality Assurance

A. Source Qualifications: CRL is ISO9001-2008 certified, with over 10 years of 	continuous manufacture of architectural glass panel sliding partition assemblies.

B. Installer Qualifications: Minimum three years of experience installing entrance 	assemblies similar to those specified in this section.

C. Single source responsibility: Obtain sliding storefront entrance systems from a single 		manufacturer, to ensure full compatibility and warranty of parts.

1.06 Delivery, Storage, and Handling

A. Deliver sliding storefront entrances and related components in the manufacturer’s 		     original protective packaging. Do not deliver entrance units until the work is ready for 	                  their installation.

B. Inspect components for damage upon delivery. Unless minor defects in metal 	components can be made to meet the Architect’s specifications and satisfaction, damaged 	parts should be removed and replaced.

1.07 Warranty

A. See Section 01 78 00 - Closeout Submittals, for additional warranty requirements.

B. See manufacturer for additional information on extended warranty periods for high 	performance coatings for track assemblies exposed to view.

PART 2 – PRODUCTS

2.01 Manufacturers

A. Series E1200 Elephant Sliding Storefront System by:

U.S. Aluminum (C.R. Laurence Company)

Tel: (800) 421-6144 or (323) 588-1281 Ext. 5305

Fax: (800) 587-7501 or (323) 584-5289

Email: 	architectural@crlaurence.com

www.crl-arch.com

2.02 Assemblies

A. Factory fabricated assemblies consisting of operable storefront system that is a 	sliding/pivoting entrance system designed and engineered with versatility and economics in 	mind. This system is suited for monumental applications requiring a sliding storefront with 	functional pivoting doors. Its heavy wall stiles and interlocks, heavy-duty tandem rollers, 	and a concealed floor track, offers smooth operation and durability. Pivoting doors 	equipped with [overhead concealed closers], [cylinder locks], [pulls] or [panics].

1. Prepared for all specified hardware whether specified in this section or not.

2. Factory assembled to greatest extent practicable; may be disassembled to 			    accommodate shipping constraints.

2.03 Performance Requirements

A. Structural Performance: shall be tested in accordance with ASTM E 330 and based on:

1. Maximum deflection of L/204 of the span

2. Allowable stress with a safety factor of 1.65

B. The system shall perform to this criteria under a windload of [Specify] psf.

2.04 Door Hardware

A. Aluminum Swing Entrance Hardware:

1. Weatherstripping: The active meeting stile of all pair of doors shall have an 	                            adjustable astragal with double line of weatherstripping.

2. Threshold: Extruded aluminum, one piece per door opening.

3. Continuous geared hinges.

4. Standard push/pull handle set.

5. Jackson overhead closer.

6. ____________ Deadbolt Lock.

7. ____________ Flush Bolts.

8. Cylinder(s).

9. Thumbturn-interior [optional].

10. Cylinder guard [optional].

2.05 Materials

A.  Extrusions shall be 6063-T5 alloy and temper ASTM B221 alloy T5 temper.

B.  Fasteners, where exposed, shall be aluminum, stainless steel or zinc plated

steel in accordance with ASTM A 164.  Perimeter anchors shall be aluminum or steel, 		      providing the steel is properly isolated from the aluminum. Glazing gaskets shall be 		      E.P.D.M. elastomeric extrusions. Door shall have a minimum wall thickness of 3/16 		      inch (4.8 mm).

C.  Glass: As specified in Section 08 80 00 Glazing; fully tempered.

1. Thickness: 1/4 inch (6 mm), or 1 inch (25 mm).

2.06 Finishes

A. All exposed framing surfaces shall be free of scratches and other serious blemishes. 	                 Aluminum extrusions shall be given a caustic etch followed by an anodic oxide  	                           treatment to obtain [Specify one of the following]:

1.  Clear anodic coating

2.  Dark Bronze anodic coating

3.  Black anodic coating

4.  A Fluoropolymer paint coating conforming with the requirements of AAMA 			     2605. Color shall be [Specify a U.S. Aluminum standard color].

PART 3 – EXECUTION

3.01 Examination and Installation

A. All glass framing shall be set in correct locations as shown in the details and shall be 	                 level, square, plumb, and in alignment with other work in accordance with the 	                           manufacturer’s installation instructions and approved shop drawings. All joints between

framing and the building structure shall be sealed in order to secure a watertight 	                           installation.

B. Do not begin installation until substrates and openings have been properly prepared.

C. If substrate preparation is the responsibility of another installer, notify Architect of 	unsatisfactory preparation before proceeding.

D. Install glass and accessories in accordance with GANA Glazing Manual.

E. Installation of door hardware not supplied by sliding storefront manufacturer is 			    specified in Section 08 71 00.

3.02 Adjusting

A. Adjust doors, to operate correctly, without binding.

B. Adjust door hardware for smooth operation.

3.03 Cleaning and Protection

A. After installation the General Contractor shall adequately protect exposed portions of 		     aluminum surfaces from damage by grinding and polishing compounds, plaster, lime, 	                 acid, cement or other contaminants. The General Contractor shall be responsible for 	                 final cleaning.

END OF SECTION